## Slide 1: ECE 571 CAN Protocol Controller Design & Verification
By
Vijay E Arputharaj
Akshay S Kotian

## Slide 2: INTRODUCTION

## Slide 3: CAN Bus
CAN(Controller Area Network) vehicle bus standard allows devices to communicate without host computer
Typical Automobile has around 70 ECU’s so communication requires robust but simple protocol
CAN, developed and patented by Bosch, fills this need

## Slide 4: Components
CPU: Host processor decides what messages to send & receive
Controller: Protocol Implementation
  Master: Packets, Serializes and transmits on bus
  Slave: Stores received bits and hands it over to CPU
Transceiver: Physical layer signaling

## Slide 5: Features
CAN is multi-master broadcast serial standard, no limitations on number of devices
Nodes have no specific address and message identifiers are content specific
CRC check for Error Handling, NRZ bit code with stuffing for synchronization
CSMA/BA(Bitwise Arbitration), prioritized arbitration with no loss in time

## Slide 6: BASIC CONCEPTS

## Slide 7: Bus Characteristics
Two Bus states
  “1” = Recessive
  “0” = Dominant
Bus logic is ‘Wired-AND’ i.e. Dominant bits overwrite Recessive bits

## Slide 8: Bus Access and Arbitration
Arbitration is non-destructive and prioritized by message
Bitwise Arbitration scheme
  Bits A[3] A[2] A[1] A[0]
  Node 1 1
  Node 2 1
  Node 3 1

## Slide 9: Bus Access and Arbitration
Arbitration is non-destructive and prioritized by message
Bitwise Arbitration scheme
  Bits A[3] A[2] A[1] A[0]
  Node 1 1 0
  Node 2 1 0
  Node 3 1 1

## Slide 10: Bus Access and Arbitration
Arbitration is non-destructive and prioritized by message
Bitwise Arbitration scheme
  Bits A[3] A[2] A[1] A[0]
  Node 1 1 0 0
  Node 2 1 0 1
  Node 3 1 1 S

## Slide 11: Bus Access and Arbitration
Arbitration is non-destructive and prioritized by message
Bitwise Arbitration scheme
  Bits A[3] A[2] A[1] A[0]
  Node 1 1 0 0 0 Bus Master!
  Node 2 1 0 1 S
  Node 3 1 1 S S

## Slide 12: Frame Formats
Data Frame

## Slide 13: Frame Formats…..
Request Frame
  - Similar to Data frame format but no Data field
Error Frame
  - Fixed Frame format sent on bus error

## Slide 14: CAN Protocol Flow

## Slide 15: IMPLEMENTATION

## Slide 16: Objective
Synthesizable Behavioral model of CAN Protocol Controller
Use System Verilog constructs for functional verification
Perform Veloce emulation in TBX mode
Designed from scratch , no existing code used