## Slide 1: ECE 571 CAN Protocol Controller: Design & Verification
By
Vijay E Arputharaj
Akshay S Kotian

## Slide 2: INTRODUCTION

## Slide 3: CAN Bus
CAN(Controller Area Network) vehicle bus standard allows devices to communicate without host computer
Typical Automobile has around 70 ECU’s so communication requires robust but simple protocol
CAN, developed and patented by Bosch, fills this need

## Slide 4: Components
CPU: Host processor decides what messages to send & receive
Controller: Protocol Implementation
  - Packets, Serializes and transmits on bus
  - Stores received bits and hands it over to CPU
Transceiver: Physical layer signaling

## Slide 5: Features
CAN is multi-master broadcast serial standard, no limitations on number of devices
Nodes have no specific address and message identifiers are content specific
CRC check for Error Handling, NRZ bit code with stuffing for synchronization
CSMA/BA(Bitwise Arbitration), prioritized arbitration with no loss in time

## Slide 6: BASIC CONCEPTS

## Slide 7: Bus Characteristics
Two Bus states
  “1” = Recessive
  “0” = Dominant
Bus logic is ‘Wired-AND’ i.e. Dominant bits overwrite Recessive bits

## Slide 8: Bus Access and Arbitration
Arbitration is non-destructive and prioritized by message
Bitwise Arbitration scheme
  Bits A[3] A[2] A[1] A[0]
  Node 1
  Node 2
  Node 3

## Slide 9: Bus Access and Arbitration
Arbitration is non-destructive and prioritized by message
Bitwise Arbitration scheme
  Bits A[3] A[2] A[1] A[0]
  Node 1 1
  Node 2 1
  Node 3 1

## Slide 10: Bus Access and Arbitration
Arbitration is non-destructive and prioritized by message
Bitwise Arbitration scheme
  Bits A[3] A[2] A[1] A[0]
  Node 1 1 0
  Node 2 1 0
  Node 3 1 1

## Slide 11: Bus Access and Arbitration
Arbitration is non-destructive and prioritized by message
Bitwise Arbitration scheme
  Bits A[3] A[2] A[1] A[0]
  Node 1 1 0 0
  Node 2 1 0 1
  Node 3 1 1 S

## Slide 12: Bus Access and Arbitration
Arbitration is non-destructive and prioritized by message
Bitwise Arbitration scheme
  Bits A[3] A[2] A[1] A[0]
  Node 1 1 0 0 0 Bus Master!
  Node 2 1 0 1 S
  Node 3 1 1 S S

## Slide 13: Frame Formats
Data Frame

## Slide 14: Frame Formats
Request Frame
  - Similar to Data frame format but no Data field
Error Frame
  - Fixed Frame format sent by all nodes on bus error

## Slide 15: Control Flow

## Slide 16: IMPLEMENTATION

## Slide 17: Objective
Synthesizable Behavioral model of CAN Protocol Controller
Use System Verilog constructs for functional verification
Perform Veloce emulation in TBX mode
Studied Bosch’s CAN specification and designed from scratch , no existing code used

## Slide 18: Design Blocks

## Slide 19: DESIGN CONSTRUCTS

## Slide 20: Packages
Parameters
Structures & Unions
Enums

## Slide 21: Interface

## Slide 22: Procedural blocks
always_ff & unique
Tasks

## Slide 23: Others….
.* operator
2 state & logic types
Queues & Associative arrays for debugging & Scoreboard
Foreach loops
Final blocks
timeunit & timeprecision

## Slide 24: Design Features
Used generate blocks to allow multiple node instantiations
All CAN specifications such as Field widths are parameterized for code reusability
Flags for Debug, Assertion, Error inject & Veloce modes

## Slide 25: VERIFICATION

## Slide 26: Assertions
Employed both immediate & concurrent assertions
Helped us immensely to localize bugs at the early stages of design as each transaction took multiple cycles, looking at waveforms or $monitor output is tedious
In the later part, developed separate assertion module which runs in parallel
Ensure nodes adhered to protocol throughout simulation and also prints out a scoreboard at end

## Slide 27: Immediate Assertions
  IFS Check:
  CRC Check:

## Slide 28: Concurrent Assertions

## Slide 29: Scoreboard (Normal Mode)

## Slide 30: Scoreboard (Error inject Mode)

## Slide 31: VELOCE EMULATION

## Slide 32: TBX Mode
XRTL Transactor configured as host processor stub for CAN nodes
Input SCEMI pipe used to get data packets generated from HVL side
Received packets, after bus transaction, are sent through output SCEMI
HVL then does scoreboard of sent and received packets and prints out log

## Slide 33: HVL
Implements Constrained Randomization & OOP techniques for generating test packets & Identifiers
Monitors received packets and produces a scoreboard at end of simulation run
Logging of input and output packets in files

## Slide 34: Randomization & OOP Constructs

## Slide 35: Scoreboard (Normal Mode)

## Slide 36: Scoreboard (Error inject Mode)

## Slide 37: Verification Features
Monitor module running concurrent assertions to trap protocol violations
Weighted randomizations allows more control on test vector generation
Randomization done on:
  Environment configuration – Multiple nodes instantiated using generate blocks and simple ID assignment algorithm employed by transactor to configure acceptance filters
  Device configuration – Random ID’s (hence randomized priority), Error injection, type of frames

## Slide 38: Summary
Build design from scratch using only a specification document
Developed test environment for generating random stimulus and scoreboard
Exercised most of the system Verilog constructs gained from the course in both design and functional verification

## Slide 39: Questions ?